## Slide 1: Cat Tracker
Steve Kennedy
NetTek Ltd

## Slide 2: What’s it all about?

## Slide 3: The hardware
1.8 x 1.2 x 0.5 inch
USB 1.1
  Logging and charging
SkyTraq Venus 5 chipset
  Sirf3, patch antenna
Battery 230mA
  runtime approx 30 hours with a 30s interval time
Logging 1s to 60m
Capacity 16,000 waypoints

## Slide 4: The hardware
Water resistant moulding
Comes with USB “dock”
2 status LEDs
  Can be disabled when tracking

## Slide 5: Attaching to cat
Can be attached to collar
Cat Harness recommended
  GPS always faces sky
Silicon mount attaches to harness
  Cat Tracker fits into mount

## Slide 6: Attaching to cat

## Slide 7: Using the data
Windows software supplied
Gets data off Cat Tracker
Data compatible with Google Maps
See where your cat’s been

## Slide 8: Cat Track Live
Contains GPS and Quad band GSM/GPRS
1.8x2.5x0.65 inches
800mAh battery
  Approx 48 hours use
“Programmed” via SMS
  Can send GPS data on demand or on set periods
Has built-in microphone
  Can call and listen

## Slide 9: Cat Track Live
Geo Fencing
  Send unit top left and bottom right lat/long
  If unit moves out of area, SMS with location is sent to authorised numbers
Move alert
  Unit stationary then send movement command
  If movement unit will indicate with position
Speed alert
  If the device moves above a set speed, it will send an alert indicating speed and location
SOS
  If the SOS button is depressed for more than 3 seconds, unit will send out an alert and location.
Low Battery alert

## Slide 10: Costs
Cat Tracker $46
Cat Harness $6
Cat Track Live $135
Available from http://www.mr-lee-catcam.de/

## Slide 11: Future
Develop kinetic charger
  Like Seiko/Citizen watch systems
  Indefinitely track objects
Used to be very difficult as GIS systems were expensive
  Google/MS/etc have made the technology easy
Now relatively easy to develop real-time geolocation based systems
  Many GSM/GPRS chipsets have built-in TCP/IP
  Use a high level programming language like Python
    i.e. unit can connect back to server over IP to report it’s position (low cost)
    Back-up over SMS

## Slide 12: Thank you for listening!
Email: steve@nettek.co.uk
p.s. No cats were harmed in producing this presentation